## Slide 2: The Spa – no issues

## Slide 3: Hawcroft.
5. Rough edges along stretch of Hawcroft. No 39-41. Well-used footway.
6. Uneven surfaces. No 5 Hawcroft
Very bumpy and patchy and uneven.
This footway in Hawcroft is well used by residents to access village amenities who do not want to walk down the B3107.
00239716 This issue does not meet the intervention levels for repair set out in Wiltshire Council's Safety Inspection Manual. ​
00239717 This issue does not meet the intervention levels for repair set out in Wiltshire Council's Safety Inspection Manual.

## Slide 4: The Midlands
7. Whole footway from Nibbs Terrace to no.4 is bumpy, patchy, uneven and inaccessible for wheelchair users. Saw people using the road.
8. Just a little along at no.2 footway breaking up from house into space for people walking.
As for Hawcroft, The Midlands is well used by residents to access amenities and dog walkers to the fields and back.
00239720 A hand patching job was raised on 25/04/25 to replace the section of footpath between numbers 2 and 5 Nibbs Terrace. It will get completed when the schedule allows. ​

## Slide 5: The Midlands
9. No. 127. Footway disintegrating and into space where people walk.
As for Hawcroft, The Midlands is well used by residents to access amenities and dog walkers to the fields and back.
00239724 This issue does not meet the intervention levels for repair​
Reported again – 00240390 A discretionary hand patching job was raised today for this section however it will be prioritised accordingly and against other worse areas as it is not considered unsafe.
10. Nibbs Terrace sign – kerb missing, trip hazard.

## Slide 6: The Midlands
11. No dropped kerbs from footway to cross the road. No clear white line markings for junction. Worrying for accessibility as this is used by vans/lorries for the industrial estate.
00239725 Very minimal wear of these give way markings, well within tolerance levels. No action required. ​
Reported again – 00240399 This issue does not meet the intervention levels for repair set out in Wiltshire Council's Safety Inspection Manual. ​
2026 additional photo

## Slide 7
7/8
10
11
9

## Slide 8: Lions Orchard – no issues

## Slide 9: The Elms
12. cracks and gaps in tarmac around drains – trip hazard